Most security systems are hard mounted and are fairly expensive. This project seeks to address both of these issues by creating a cheap system that can be temporarily mounted.

OVERVIEW OF HARDWARE

Arduino uno connected to a WiFi Shield, An Ultrasonic sensor, A SR latch which controls the relay and A relay that is connected to whatever the user wants, for the purpose of this demonstration it is connected to a led.

DEMONSTRATION: SETTING DISTANCE

The distance is set by first accessing the web interface for the device and then clicking the “set distance” button. This will pulse the ultrasonic sensor 4 times and take an average of the measurements.

DEMONSTRATION: ALARM

if the device is in alarm mode, it will trigger the alarm whenever it detects 2 measurements outside the set threshold as demonstrated in the serial monitor.

DEMONSTRATION: RELAY

the relay on the device can be triggered from the web interface. This acts a toggle switch between the latched and unlatched relay modes.

DEMONSTRATION: MOTION ACTIVATED RELAY

this setting works of the same measurements as the alarm but instead of sounding the alarm it will toggle the relay on for 60 seconds then turn it off. This works like motion detecting garden lights and will set the timer back to 60 every time it detects something.

DEMONSTRATION: MOUNTING LOCATIONS

since one of the criteria for the device was soft mounting, the device has no mounting hardware attached to it but due to the lightweight nature of the device, it can be attached using temporary solutions such as sellotape or velcro. The device also functions just as well placed upon a pile of books, on the floor or anywhere else that faces a door.